# Procedure for Boot Loading AT328 Chip
## Loading Arduino ISP Sketch:
Connect the Boot Sheild to Arduino and place the new AT328 IC to Jig base as shown below.
Arduino with BootSheild
Open Arduino ISP Skectch by, selecting File->Examples->11.ArduinoISP-> ArduinoISP and upload the sketch to arduino.
Opening Arduino ISP Sketch
Uploading to Arduino
## Identifing COM Port:
Press “Win+R” to open Run, and type devmgmt.msc command to open Device Manager.
Run
Device manager
Note down the Serial Port to which arduino is connected. (In the above screen shot it is COM3).
## Edit the Script File:
To edit the script file, right click on the file (Load-BL-AT328-xVyz.bat), and select edit and a notepad will open as shown below.
Right Click Menu
Changing COM Port

Now change the COM port number to the port to which Arduino is connected (ie Previous Step) and save and close the file.
## Loading BootLoader:
Go to the folder where the “Load-BL-AT328-xVyz.bat” file is present, and type cmd in the address bar and press enter to open command prompt.
Boot Loader Script Folder
Command Prompt
In Command Prompt, type Load-BL-AT328-1V00.bat and press enter to load the boot loader. Refer the below screen shot

Script Output